## Slide 1: GB Demand forecasting
Time-Series

## Slide 2: Thoughts on Time-Series Forecasting
The parameters of your time-series model should reflect the real-world impact of variables on the dataset, independent of the model’s algorithm.
  Therefore, different parameters of the same model convey different views and insights of the dataset.
Models | Details | Examples
Decomposition-based | Deconstruction of time series into components: Trend, Seasonalities, Regressors, Residuals. | Prophet, Exponential Smoothing (Holt-Winters).
ARIMA-based | Autoregressive (AR) terms {values}, differencing to achieve stationarity (I), and moving average (MA) terms {residuals}. | SARIMA, SARIMAX, GARCH, etc.
Neural Networks | Use of Transformers, Recurrent Neural Networks (RNN), Convolutional Neural Networks (CNN) | Long Short-Term Memory (LSTM), Temporal Convolutional Networks (TCN)
Ensemble methods | Combines forecasts from multiple models to improve accuracy. | -
Notes: GB Demand with a more flexible trend change might give better insights of the weekly distribution, weather impact, etc. and would most probably forecast the future with higher accuracy. {Good insights into profiling}
GB Demand with small trend changes will give a better view of the long-term impacts of variables affecting the volumes consumed: Efficiency, GDP, Population, Energy Prices, COVID restrictions…
Decomposition-based: Good for understanding of the components and time-series that have seasonalities – therefore: affected by patterns (humans, plants, animals) >> Non-linearities for seasonality.
ARIMA-based: Explainability and very good for non-seasonal data >> although no non-linearities.
Neural Networks:
  Transformers use self-attention to capture relationships between all time points simultaneously, handling long-term dependencies well in time-series forecasting.
  RNNs process time-series data sequentially, using past information to predict future values, effective for capturing short to medium-term dependencies.
  CNNs apply filters to time-series data to detect local patterns and trends, useful for extracting features and short-term dependencies in forecasting.
Transformers
1. Mechanism: Use self-attention to process all time points simultaneously.
2. Strength: Excellent at capturing long-term dependencies.
3. Efficiency: Can handle very long sequences efficiently due to parallel processing.
4. Complexity: Generally more complex and resource-intensive.
Recurrent Neural Networks (RNNs)
1. Mechanism: Process sequences sequentially, passing information from one step to the next.
2. Strength: Good at handling sequential data with short to medium-term dependencies.
3. Efficiency: Can struggle with long sequences due to issues like vanishing gradients.
4. Complexity: Simpler than transformers, but can become complex with layers like LSTM or GRU for improved long-term dependency handling.
Convolutional Neural Networks (CNNs)
1. Mechanism: Apply filters to detect local patterns and features.
2. Strength: Effective at capturing short-term dependencies and local trends.
3. Efficiency: Efficient at processing data in parallel, but mainly captures local context.
4. Complexity: Less complex than transformers, relatively straightforward to implement.

## Slide 3: Why Prophet? in Power Demand Forecasting
Open-box: Clear input components, parameters, outputs, optimization algorithm - not neural networks.
  Trend, Daily/Weekly/Yearly Seasonality, Holidays, External variables.
Uses “non-linear” algorithms for seasonality– but can be optimized as a linear model (Fourier Series).
Robustness to missing data and outliers:
  Data missing handling + Fitting downweighs outliers + L1 loss function > minimizes absolute deviations, not squared + Bayesian inference by sampling instead of MLE for posterior distributions.
Notes: Data missing > out of the optimization problem >> Anyway all the seasonalities are continuous functions, depicting the intrinsic dependence on previous datapoints.
L1 loss function instead of L2 for downweighing outliers.
MCMC (Markov-Chain Monte Carlo): To get posterior distributions (1000 iterations by default) – State-dependent Bayes Method ran many times.
  This is optional. If not used, the prior distributions are used.

## Slide 4: GB Gross Demand ETL ELEXON**
1. Getting needed dataflows:
- D0043: GSP Group Correction Factors.
- D0018: Profile Class Coefficients.
- DXX: Transmission Loss Multipliers.
- D0265: Line Loss Factors.
2. Processing P315 Reports using previous dataflows:
- P0276: GSP Group Consumption Reports (HH-metered).
- P0277: Group Market Matrix Report (NHH-metered)
3. Processing T-connected and D-connected Demand
- Grouping NHH and HH metered data + sectoral split by CCC (Consumption Component Class)  P315 Gross GSP Demand.
- Processing T-connected demand data (half-hourly) from the CDCA-I042 dataflow.
4. Merging the GSP gross demand data with the T-connected demand data
- Total GB Gross Demand by GSP, half-hourly granularity.
HH: Half-Hourly.
NHH: Non-HH
GSP: Grid Supply Point
Notes: https://github.com/pcpp94/elexon_pipeline_GB_demand

## Slide 5: Weather Data ETL Meteostat**
['Kinloss', 'Wick', 'Aberdeen / Dyce', 'Eskdalemuir', 'Leuchars', 'Leeming', 'Waddington', 'Shawbury', 'Aberporth', 'Lyneham', 'London Heathrow Airport', 'Manston', 'Camborne', 'Bournemouth Airport']
Mapping the closest weather stations to each GSP area

## Slide 6: Different Granularities, Different Insights…
Hourly:
- Weather impact on the hourly volume ± (daily shape).
- Seasonality impact on the hourly volume.
- Holiday impact on the hourly volume ± (daily profile).
- Change of the daily shape throughout the weeks, months, years.
Daily:
- Weather impact on the daily volume.
- Seasonality impact on the daily volume.
- Holiday impact on the daily volume.
*Faster to run – straight forward analysis on the impact of holidays on demand.
Monthly:
- Weather/Holidays corrected demand is used as an input (Taking away weather effects and conveying a cleaner timeseries)
- Having these “weather/H-adjusted” volumes allows us to use available indicators as regressors:
(GDP for the Non-domestic demand)
(Population + Prices for the Domestic demand)
Choosing depends on: Data granularity, Compute power, Analysis Requirements.
Notes: GB Demand with a more flexible trend change might give better insights of the weekly distribution, weather impact, etc. and would most probably forecast the future with higher accuracy. {Good insights into profiling}
GB Demand with small trend changes will give a better view of the long-term impacts of variables affecting the volumes consumed: Efficiency, GDP, Population, Energy Prices, COVID restrictions…

## Slide 7: Granular Forecasting
Prophet

## Slide 8
Hyper-parameter tuning
Regularization of Objective Function’s coefficients.
Time Series
Signal
Noise [Error]
Signal Breakdown
Trend
Yearly Seasonality
Weekly Seasonality
Holidays
Weather
Regressors
Non-Domestic Daily Model
Notes: Out of:
14 GSP areas
Domestic/Non-domestic by area.
Understanding the impact of all these Daily // Hourly if you have // variables altogether.

## Slide 9
Hyper-parameter tuning
Regularization of Objective Function’s coefficients.
Time Series
Signal
Noise [Error]
Non-Domestic Daily Model
Noise [Error]
Temperature Regressors
Overcoming linear constraints
Forecast + Trend Changepoints
Example of very straightforward analysis enabled by decomposing Demand.
The GWh/GDP ratio shows that the level of efficiency gains / behind-the-meter deployment has remained relatively constant.
Chart: 
Notes: Out of:
14 GSP areas
Domestic/Non-domestic by area.

## Slide 10
Hyper-parameter tuning
Regularization of Objective Function’s coefficients.
Time Series
Signal
Noise [Error]
Non-Domestic Daily Model
Noise [Error]
Temperature Regressors
Overcoming linear constraints
Example of very straightforward analysis enabled by decomposing Demand.
The GWh/GDP ratio shows that the level of efficiency gains / behind-the-meter deployment has remained relatively constant.
Chart: 
Notes: Out of:
14 GSP areas
Domestic/Non-domestic by area.

## Slide 11
Hyper-parameter tuning
Regularization of Objective Function’s coefficients.
Time Series
Signal
Noise [Error]
Non-Domestic Daily Model
Noise [Error]
Temperature Regressors
Overcoming linear constraints
Forecast + Trend Changepoints
Notes: Out of:
14 GSP areas
Domestic/Non-domestic by area.

## Slide 12: Prophet Objective Function
Adjustments at changepoints j
Forecasting – Decomposable time-series model
Trend Function
[Scalar] [Vector] [Vector] [Scalar] [Vector]
Seasonality Function
[Scalar for each n]
[Scalars for each n]
[Scalars for each n]
Example: Yearly
Holidays
Same concept for the included regressors.
[Scalars for each i]
[Scalars for each i]
Notes: SHOWING:
The MODEL PARAMETERS, which are the coefficients of the different functions within the objective functions.
a(t):
a_t is a binary vector where each element indicates whether time t is after the corresponding changepoint.
- For example, if there are changepoints at times t_1 and t_2 , then:
a_t = [I(t > t_1), I(t > t_2)]
where I is an indicator function that returns 1 if the condition is true and 0 otherwise.

## Slide 13: Regularization + Objective Function
The objective function includes regularization terms to penalize the complexity of the model:
𝑃𝑒𝑛𝑎𝑙𝑡𝑦 = 𝜆𝛿 ||𝛿||₂² + 𝜆a ||||₂² + 𝜆b ||||₂² + 𝜆 ||||₂²
where: 𝜆𝛿: 𝐶ℎ𝑎𝑛𝑔𝑒𝑝𝑜𝑖𝑛𝑡 𝑝𝑟𝑖𝑜𝑟 𝑠𝑐𝑎𝑙𝑒. 𝜆a : 𝑆𝑒𝑎𝑠𝑜𝑛𝑎𝑙ity 𝑝𝑟𝑖𝑜𝑟 𝑠𝑐𝑎𝑙𝑒𝑠. 𝜆b : 𝑆𝑒𝑎𝑠𝑜𝑛𝑎𝑙ity 𝑝𝑟𝑖𝑜𝑟 𝑠𝑐𝑎𝑙𝑒𝑠. 𝜆: 𝐻𝑜𝑙𝑖𝑑𝑎𝑦 𝑝𝑟𝑖𝑜𝑟 𝑠𝑐𝑎𝑙𝑒.
The objective is to minimize the sum of the errors (residuals) plus the regularization penalties:
where: is the fitted value at time t.
The penalties on , , , and discourage large coefficients, resulting in a smoother trend and seasonal components that better generalize to new data.
L1 loss function is more robust to outliers because it penalizes them linearly, whereas L2 (Ridge Regression) penalizes them quadratically.
Notes: SHOWING:
The MODEL HYPERPARAMETERS, which affect the model parameters quadratically to make them smoother > Regularization L2 here.
To explain the L2 in minimizing the objective function:
The functions is minimizing the ERRORS, which depend on different values for each variable.
However, the L2 affects all variables in the same way, it makes them be lower.
Therefore, it ends up smoothing and making these coefficients sensible numbers, not super large.

## Slide 14: Objective Function and Main Hyperparameters
Adjustments at changepoints j
Trend Function
∼ Laplace(0, τ )
Seasonality Function
Example: Yearly
Holidays
Same concept for the included regressors.
where: is the fitted value at time t.
𝜆𝛿: 𝐶ℎ𝑎𝑛𝑔𝑒𝑝𝑜𝑖𝑛𝑡 𝑝𝑟𝑖𝑜𝑟 𝑠𝑐𝑎𝑙𝑒. 𝜆a : 𝑆𝑒𝑎𝑠𝑜𝑛𝑎𝑙ity 𝑝𝑟𝑖𝑜𝑟 𝑠𝑐𝑎𝑙𝑒𝑠. 𝜆b : 𝑆𝑒𝑎𝑠𝑜𝑛𝑎𝑙ity 𝑝𝑟𝑖𝑜𝑟 𝑠𝑐𝑎𝑙𝑒𝑠. 𝜆: 𝐻𝑜𝑙𝑖𝑑𝑎𝑦 𝑝𝑟𝑖𝑜𝑟 𝑠𝑐𝑎𝑙𝑒.
These are the hyperparameters directly affecting the coefficients of the Objective Function.
coefficient
coefficients
coefficient
Hyperparameters
Notes: Showing the coefficients being affected by the hyperameters.

## Slide 15: All the Hyperparameters.
seasonality_prior_scale: [0.01, 10] default 10
holidays_prior_scale: [0.01, 10] default 10
changepoint_prior_scale: [0.001, 0.5] default 0.05
mcmc_samples: [boolean] default ‘false’
changepoint_range: [0.8, 0.95] default 0.8
seasonality_mode: [‘additive’, ‘multiplicative’] default ‘additive’
changepoints: [dates] default None
yearly_seasonality: [boolean] default ‘auto’
n_changepoints: [integer number] default 25
weekly_seasonality: [boolean] default ‘true’
daily_seasonality: [boolean] default ‘auto’
holidays: [DataFrame] default None
interval_width: [0.8, 0.95] default 0.8 {confidence level}
uncertainty_samples: [integer number] default 1000
Tune-able
growth: [‘linear’, ‘logistic’] (saturation point?) default ‘linear’
Usually not tune-able
Using MCMC
For trend, seasonalities, regressors, holidays, forecast
Notes: Regarding the interval_width / confidence level:
Imagine Prophet forecasts that you’ll sell 100 ice creams tomorrow with an 80% uncertainty interval from 90 to 110. This means:
• Most Likely Range: There’s an 80% chance you’ll sell between 90 and 110 ice creams.
>> What do we want to show? What level of confidence in our forecast and the different components?
Model Parameters
growth: String specifying the type of trend to fit. Either 'linear' or 'logistic'.
changepoints: List of dates at which to include potential changepoints. If not specified, potential changepoints are automatically selected.
n_changepoints: Number of potential changepoints to include.
changepoint_range: Proportion of the history in which trend changepoints will be estimated. Defaults to 0.8 for the first 80%.
Trend Parameters
changepoint_prior_scale: Parameter controlling the flexibility of the automatic changepoint selection. Larger values allow for more changepoints.
seasonality_prior_scale: Parameter controlling the strength of the seasonality model.
holidays_prior_scale: Parameter controlling the strength of the holiday components.
mcmc_samples: If greater than 0, will do full Bayesian inference with the specified number of MCMC samples. Defaults to 0 for MAP estimation. [MCMC: Markov Chain Monte Carlo]
interval_width: Width of the uncertainty intervals provided for the forecast. Defaults to 0.8.
Seasonalities
seasonality_mode: Either 'additive' (default) or 'multiplicative'.
yearly_seasonality: Boolean or integer. If True, include yearly seasonality (default). If False, no yearly seasonality. If an integer, specify the Fourier order.
weekly_seasonality: Boolean or integer. Similar to yearly_seasonality, but for weekly data.
daily_seasonality: Boolean or integer. Similar to yearly_seasonality, but for daily data.
seasonality_prior_scale: Parameter controlling the strength of the seasonality model.
Holidays and Events
holidays: DataFrame with columns holiday (name of the holiday), ds (date of the holiday), and optionally lower_window and upper_window for adding days around the date as holiday effect.
holidays_prior_scale: Parameter controlling the strength of the holiday components.
Others 1. uncertainty_samples: Number of simulated draws used to estimate uncertainty intervals.

## Slide 16: Model Fitting, Posterior Distribution
Most calculations use Bayesian inference, more specifically: Posterior log-likelihood.
  We clearly want the residuals to be follow a normal distribution  We might as well input and use that information.
Logarithm of the posterior probability (the Log transforms products into a sum, less computationally intensive).
Log-likelihood is used for:
  Model fitting through Bayesian inference.
  Optimization for MAP Estimation.
  MCMC Sampling for Posterior Distribution.
Optimization Algorithm used by default:
  Penalized maximum likelihood estimation with optimization (L-BFGS)
Example of a linear regression using L-BFGS
Posterior log-likelihood
Notes: Posterior Log-Likelihood == Logarithm of the posterior probability.
Combines:
  How well the model fits the data (likelihood).
  Prior beliefs about the parameters (priors).

## Slide 17: MAP vs. MCMC
Both infer parameters based on observed data and prior beliefs.
  MAP: Maximum a Posteriori estimation.
    Conveys a single point estimate: maximum posterior distribution.
    It’s an optimization problem (often GD).
    In complex scenarios, it might miss multiple modes in the posterior.
  MCMC: Markov Chain Monte Carlo sampling.
    Conveys a collection of samples representing the posterior.
    It’s a stochastic simulation.
    Can capture multi-modality in the posterior.
Notes: The posterior probability distribution is the updated probability of a parameter after observing data, combining prior beliefs with the likelihood of the observed data using Bayes’ theorem.
MAP Estimation Steps:
1. Define the likelihood P(D | \theta) and prior P(\theta).
2. Compute the posterior P(\theta | D) \propto P(D | \theta) P(\theta).
3. Find \theta_{\text{MAP}} = \arg\max_{\theta} P(\theta | D).
MCMC Sampling Steps:
1. Define the likelihood P(D | \theta) and prior P(\theta) .
2. Set up an MCMC algorithm (e.g., Metropolis-Hastings) to sample from P(\theta | D) .
3. Generate a large number of samples \{ \theta^{(i)} \} .
4. Analyze the samples to estimate quantities of interest (mean, variance, credible intervals).

## Slide 18: Seasonality using Fourier Series

## Slide 19: Understanding the Python Model: Initial Parameters
model.preprocess(df):
'K’: number of variables' coefficients.
'S’: number of slope changes (at each changepoint)
'T’: Number of time series’ datetime points.
'X': Dataframe of TxK (each time series datetime point x the variables’ coefficients as columns).
'cap': for logistic growth.
's_a': additive terms.
's_m': multiplicative terms.
'sigmas': Coefficients' prior_scales (Hyperparameters)
't': time.
't_change': value of t at changepoints.
'tau': changepoint prior_scale >> flexibility.
’y’: standardized y values.
Notes: Within Prophet package:
model_inputs: values, inputs, inputted into the model, that are not going to change through modelling. (model.calculate_initial_params())
intial_params: intial parameters that will change through iterations of the optimization. (model.params)
'K’: number of variables' coefficients [BETA size in model.params].
'S’: number of slope changes (at each changepoint) [DELTA size in model.params].
'T’: number of estimated values of the trend component of the time series at each time point. [TREND size in model.params].
'X': Dataframe of TxK (each time series datetime point x the variables’ coefficients as columns).

## Slide 20: Understanding the Python Model: Fitted Parameters
Lp__(Mx1): Log posterior density of the model parameters.
k (Mx1): Growth rate parameter / slope.
m (Mx1): Initial intercept / offset parameter: starting point of trend.
delta (MxN): Slope change at each changepoint.
sigma_obs (Mx1): Standard deviation of the observations.
beta (MxK): Coefficients for seasonalities, holidays, regressors.
trend (MxT): Estimated trend at each datetime.
Where:
M: number of posterior samples.
N: number of changepoints.
K: number of coefficients (seasonalities, holidays, regressors).
T: number of timestamps in the time series.
Notes: Within Prophet package:
- model_inputs: values, inputs, inputted into the model, that are not going to change through modelling. (model.calculate_initial_params())
- intial_params: intial parameters that will change through iterations of the optimization. (model.params)

## Slide 21: Stan Optimization Algorithm
“double_exponential(0,tau)” is a Laplace(0, tau) distribution.
Stan code

## Slide 22: HyperOpt: Hyperparamter tuning
We are using HyperOpt to tune the hyperparameters
  https://github.com/hyperopt/hyperopt
  The algorithm we are using is TPE (Tree-based Parzen Estimators)
    Sequential Model-Based Optimization (SMBO) that handles complex hyperparameter relationships via a tree structure.
    More details: https://towardsdatascience.com/hyperopt-demystified-3e14006eb6fa
TPE is a sequential algorithm that leverages Bayesian updating and follows the below sequence.
  Train a model with several sets of randomly-selected hyperparameters, returning objective function values.
  Split our observed objective function values into “good” and “bad” groups, according to some threshold gamma (γ).
  Calculate the “promisingness” score, which is just P(x|good) / P(x|bad).
  Determine the hyperparameters that maximize promisingness via mixture models.
  Fit our model using the hyperparameters from step 4.
  Repeat steps 2–5 until a stopping criteria.

## Slide 23: Training Prophet Models
When cross_validating horizons need to be longer than longest seasonality

## Slide 24: TO SHOW
Error plots by variables (by DOW, by temperature).
Explaining what each variable means.
Explaining what the trend means under the inputted variables.
Why using a granular (Daily or Hourly) and Monthly models separately makes sense.
  Utilize the most granular, reliable and important variables (example: GDP > monthly).
  Noise creation.
Notebooks?

## Slide 25: Some GB demand insights
The north of the country has a higher heating demand [%] than the south during winter. However, its demand varies less with colder temperatures (2015-2023 data).
  Domestic: There is higher potential to shift winter demand down South apparently. There isn’t more "electric heating" down South to explain the higher regressors’ magnitude during cold temperatures.
  Non-Domestic: Quite a lot aircon demand that could be shifted in summer.

## Slide 26: Hourly Modelling
Next article will go into tackling Hourly granularity modelling using Prophet.
Graph showing weather effect at different hours:

## Slide 27: Prophet inherent drawbacks
Overcoming linearity:
  Seasonality is inherently non-linear: Fourier Series.
  Regressors are linear, we need to make them depict non-linearities
    Thought: maybe using temperature ^ 2 or something? Explore.
Hyperparameters optimization: HyperOpt.
Holidays not considering DOW.
Weekly Seasonality change through year (Mostly Sat, Sun in GB).
Regressors are standardized around the mean.